## Slide 1
Automated Greenhouse Monitoring System
Prepared by: Bits Wizards Team

## Slide 2
Our Team
Mostafa Edress
Samar Ibrahim
Fathy Anas

## Slide 3
Download

## Slide 4
Table Of Content
Overview
System Architecture
Project Layers
Result

## Slide 5
Maintaining optimal greenhouse conditions is essential for healthy plant growth and maximizing yield. Manual monitoring and adjusting of temperature, humidity, light, and soil moisture can be labor-intensive and error-prone, leading to inconsistent growing conditions. To ensure reliable and efficient greenhouse management, an automated solution is needed to optimize the monitoring and control of these environmental factors.
Project Overview

## Slide 6
Project goals
To develop an Automated Greenhouse Monitoring System that ensures optimal growing conditions for plants by automating the monitoring and control of environmental factors such as temperature, humidity, light, and soil moisture.

## Slide 7
Sensor Module
Microcontroller Units (MCUs)
Display Unit
Control Unit
System Architecture
Alert System
Soil Moisture Sensor
Light Intensity Sensor
DHT11 Sensor
Master MCU:
Reads sensor data.
Controls fan, heater, pump, and LED.
Slave MCU:
Displays data on a 20x4 LCD.
Send data to Node red Server
Node Red Server
Fans and Heaters: Manage temperature.
Irrigation System: Controls soil moisture.
Grow Lights: Regulates light intensity.
Buzzer
Red led
to generate alerts if values go out of the optimal range.
LCD 20*4
Send notification to the user on mobile app

## Slide 8
Microcontroller Abstraction Layer
1
  Hardware Abstraction Layer
  2
  Library Layer
  4
  Application Layer
  3
  Service Layer
  5
Project Layers

## Slide 10
Application Layer
Automatic Control: Regulates heating, irrigation, and lighting systems.
AGMS: Coordinates sensors, automatic control, display units, and communication systems
Display: Manages data visualization on LCD and Node-RED.
Sensors: Integration and management of various sensors

## Slide 11
Services Layer
I2C Communication Frame: Manages data transmission with checksum for data validation
Node-RED Communication: Handles data transfer to Node-RED server, provides remote monitoring

## Slide 12
Project Schematic on Proteus

## Slide 13
Normal
Error
Temperature :18->26
Humidity :40->70
Soil moisture :30->60
Light intensity:45->75
Temperature :<10 or >40
Humidity :<20 or >80
Soil moisture :<10 or >80
Light intensity:<20 or >90
Range of Normal and Error State

## Slide 14
Node Red Dashboard

## Slide 15
Node Red Dashboard

## Slide 16
Final Output

## Slide 17
Thank
You